## Slide 1: AUTOSAR Application & RTE
By: Hassan Farahat

## Slide 2: Agenda
Intro to RTE
SWC Design
RTE Deep Dive (SR, CS, MS)
RTE Configuration & Generation

## Slide 3: Tasks
Sprints AUTOSAR
Authoring Tool (SAAT)
Task 1: High Level Design
Task 2: Sender Receiver
Task 3: Client Server
Task 4: Types of SWCs
Task 5: Mode Switch
Task 6: RTE Configuration & Generation

## Slide 4: Get in Touch
Contact
LINKEDIN PROFILE
https://www.linkedin.com/in/hassan-farahat-77289477/
PHONE (WhatsApp)
+201092439690
EMAIL
hassan.m.farahat@gmail.com

## Slide 5: Virtual Function Bus
Intro to AUTOSAR Application
Virtual Functional Bus (VFB)
VFB Quiz

## Slide 6: AUTOSAR Layers
Application
RTE
BSW

## Slide 7: Application Layer
- The top layer in AUTOSAR software architecture
- Many Applications drive the Vehicle System
- Examples
- OBC (On Board Charger)
- ADAS (Automated Driving and Driver Assistance)
- V2X (Vehicle-to-everything) applications

## Slide 8
CAN/LIN/Eth/FlexRay
SWC
SWC
SWC
SWC
ECU 1
ECU 2
ECU N
. . . .
SWC
SWC
SWC
SWC
SWC
SWC
SWC
SWC
Application is a group of components, interacting together to achieve specific feature
Software components of the same application can be distributed over different ECUs in the Vehicle System

## Slide 9: Challenges
1. Application must fit in different Vehicle hardware and systems for the same OEM or even for different OEMs
Application shall be hardware and system independent

## Slide 10: Challenges
2. Application development is time consuming, containing the main software (Logic / Algorithms)
Application development shall be accelerated as much as possible

## Slide 11: Challenges
3. Application features shall be adapted based on OEM requirements
Application shall be maintainable/scalable
So AUTOSAR introduced
Virtual Function Bus (VFB)

## Slide 12: Virtual Function Bus
Intro to AUTOSAR Application
Virtual Functional Bus (VFB)
VFB Quiz

## Slide 13: What is VFB?
SWC
Virtual Functional Bus Layer
VFB_Write_CarSpeed
VFB_Read_CarSpeed
VFB_NvMWrite_CarSpeed
VFB_GetSensorValue
System
Hardware (i.e., Sensors)
BSW
VFB_Schedule(10ms)
MCU
SWC
SWC
SWC

## Slide 14: What is VFB?
- VFB is a modeling for application components to interact together through Virtual Connections
- Thanks to the virtual connections, the application components are strictly separated from the infrastructure (hardware, sensors, system .. etc.)

## Slide 15: VFB Description
- Communication with other SWCs in the System
- Communication with Sensors and Actuators
- Communication with Standard services (i.e., Writing and Reading from NvM)
- OS Scheduling (i.e., Cyclic Functions)
Through VFB, you can describe:

## Slide 16: VFB Simulation
https://www.yumpu.com/en/document/read/11123332/virtual-functional-bus-simulator-autosar
VFB simulation tools provides application development and testing env on PC

## Slide 17: More about VFB
Read more about VFB concept in AUTOSAR:
https://www.autosar.org/fileadmin/standards/R20-11/CP/AUTOSAR_EXP_VFB.pdf

## Slide 18: Virtual Function Bus
Intro to AUTOSAR Application
Virtual Functional Bus (VFB)
VFB Quiz

## Slide 19: VFB Quiz
Test the real time behavior
Do unit testing for SWCs
Test memory consumption (stack, ram, rom)
Test external bus communication
Simulate Intra-ECU communication
Simulate Inter-ECU communication
Using VFB Simulation, the App Developer can:

## Slide 20: VFB Quiz: Solution
Test the real time behavior
Do unit testing for SWCs
Test memory consumption (stack, ram, rom)
Test external bus communication
Simulate Intra-ECU communication
Simulate Inter-ECU communication
Using VFB Simulation, the App Developer can:

## Slide 21: Run Time Env (RTE)
What is RTE?
Development Workflow

## Slide 22: VFB Deployment
- Virtual connections between SWCs has to be mapped either to local connections (same ECU) or network connections (i.e., through CAN/LIN on different ECUs)
- VFB Sensors/Actuators are mapped to the real hardware
- Standard Services are mapped to the BSW Services
- Windows Threads Scheduling are mapped to AUTOSAR Tasks
On deployment of VFB model description into new System:

## Slide 23: VFB Deployment
That mapping is done through RTE
RTE modules on all ECUs represents the VFB layer deployment on the vehicle system

## Slide 24
The entire communication of SWCs is based on the VFB
So, SWCs are independent of the ECU hardware/System
So, SWCs can be reused across different systems/platforms
The VFB is implemented for a specific vehicle by supplying a specifically configured RTE
C# impl for:
VFB_GetSensorValue
VFB_Read_CarSpeed
VFB_Write_CarSpeed
VFB_NvMWrite
….
Rte C impl for:
Rte_GetSensorValue
Rte_Read_CarSpeed
Rte_Write_CarSpeed
Rte_NvMWrite
….
RTE (Run Time Environment) is the AUTOSAR Layer that implements the VFB Concept

## Slide 25: Why RTE?
1. Application must fit in different Vehicle hardware and systems for the same OEM or even for different OEMs
Application is hardware/system independent as it is abstracted by the RTE APIs,
For each System, it is the same App Code, but different RTE,
AUTOSAR Application shall use only RTE for any types of communication

## Slide 26: Why RTE?
2. Application development is time consuming, containing the main software (Logic / Algorithms)
Application development and testing can be done even before developing the Vehicle System
Interaction with the real hardware, interaction with the BSW, interaction with other ECUS .. etc. all handled by the RTE
Application run time behavior is managed by the RTE (Scheduling, Variables protection .. etc.)
Application developer shall only think about writing the application logic

## Slide 27: Why RTE?
3. Application features shall be adapted based on OEM requirements
SWCs can be added/removed without affecting the other software components / other features in the Vehicle

## Slide 28: Run Time Env (RTE)
What is RTE?
Development Workflow

## Slide 29: Workflow
VFB Tools are usually used by OEM for complete system design and simulation
In the next slides, we will start with RTE Workflow directly, which is the common case in Tier 1,2 suppliers

## Slide 30: RTE Workflow
App Design
Application Description
Arxml Files
Contract Phase
App Templates
App Code
Develop

## Slide 31
- Description for the application components, that defines the application needs/interfaces from the RTE
- Description is created using Authoring Tools and saved in AUTOSAR XML file (.arxml)
- The xml schema used to create the arxml file is called Software Component Description “SWCD”, and can be found on autosar.org
App Design
Application Description
Arxml Files

## Slide 32: Application Description
AUTOSAR Schema
XML hierarchy and elements as defined by the Schema

## Slide 33: Application Description
Example: Create SWCD for “ChrgMgr” component
ChrgMgr shall control the electric charging for the Vehicle
Software Component Description: ChrgMgr shall need the following interfaces:
Interface to read the current battery level
Interface to read the max power that can be provided from the charging station
Interface to start/stop charging
ChrgMgr
BatteryLevel
MaxPower
Invoke Charge(start/stop)
ChrgMgr.arxml
Authoring Tool

## Slide 34
- Application templates with prototype of the standard interfaces that will be provided from the Rte
- Templates are generated from Authoring Tool
- App Developer shall base app code on these templates
- Thanks to the standard interfaces, the application code will be the same regardless the Vehicle System
Arxml Files
Contract Phase
App Templates

## Slide 35: Contract Phase
Contract Phase for ChrgMgr_Template.c
RTE Interfaces Provided to ChrgMgr SWC, as per the SWCD

## Slide 36
- Use the generated templates to develop the
code for all software components
App Templates
App Code
Develop

## Slide 37: Develop
ChrgMgr Code (ChrgMgr.c)
SWC Logic

## Slide 38
Reusable Application!
Reuse on different systems

## Slide 39: Reuse
RTE Generator
Rte.c
Compile
HEX
New System
RTE Generator
Rte.c
Compile
HEX
RTE Generator
Rte.c
Compile
HEX
ECU 1
ECU 2
ECU N
ChrgMgr.arxml
ChrgMgr.c
Same Application on Different Systems
Same ChrgMgr.c, Different Rte.c

## Slide 40
CAN/LIN/Eth/FlexRay
SWC
. . . .
ChrgMgr
SWC
SWC
ECU 1
ECU 2
ECU N
Rte
Rte
Rte
BSW
BSW
BSW
SWC
ChrgMgr
SWC
SWC

## Slide 41: SWC Design
SWCD High Level Design – Task 1
SWCD Impl Level Design
SWCD Data Types
SWCD Conclusion

## Slide 42
- AUTOSAR Application is described to the Rte in the format of “.arxml” file
- The schema used to create the arxml file is called “SWCD”, and can be found on autosar.org
- Application arxml file(s) shall contain the SWCD for all application software components
SWCD
Software Component Description

## Slide 43
- Authoring Tools provide Graphical User Interface (GUI) to create arxml files and also generating the SWC templates
- Most common Authoring Tools
- DaVinci Developer (Vector)
- System Desk (dSpace)
- AUTOSAR Builder (3ds)
- SAAT (Sprints)
SWCD
Authoring Tools

## Slide 44: Atomic Components
- AUTOSAR Application is organized in Units called Atomic Software Components “SWC”
- Each SWC encapsulates the implementation of its functionality and behavior
- “Atomic” as the software component can’t be distributed on multiple ECUs
- SWC can communicate with the outside world using Ports
Application Components

## Slide 45: Ports
- Each Software component define its inputs from other components and outputs to other components using Ports
- Port can be either Provided Port (Output) or Required Port (Input)
- Provided Port: SWC is providing a service or data
- Required Port: SWC is requires a service or data
- Each Port is typed by “instance of” Port Interface

## Slide 46: Port Interface
- Port Interface define the type of communication between SWCs
- Common types of communication: Sender Receiver Communication and Client Server Communication
- Sender Receiver: Data exchange between SWCs
- Client Server: Operation “function” exchange between SWCs

## Slide 47: Sender Receiver
- Sender Receiver Interface is used to share data between SWCs
- Sender :: SWC providing the data (Provided Port)
- Receiver :: SWC requires the data (Required Port)
Sender Receiver Interface:
Data Elements “Type, Name”

## Slide 48
SWC1
SWC2
SrIf_VehicleData
uint32 VehicleSpeed
ppVehicleData
rpVehicleData
Rte_Write_ppVehicleData_VehicleSpeed(uint32 VehicleSpeed);
Rte_Read_rpVehicleData_VehicleSpeed(uint32* VehicleSpeed);

## Slide 49: Client Server
- Client Server Interface is used to share operation “function” between SWCs
- Client :: SWC requires “invokes” the operation (Required Port)
- Server :: SWC providing the operation (Provided Port)
Client Server Interface:
Operation Prototype “Name, Args, Return”

## Slide 50
Rte_Call_rpChrgCtrl_StartCharging(uint32 TargetBatLvl);
Client
Server
Client Server Interface:
void StartCharging(uint32 TargetBatLvl)
ppChrgCtrl
rpChrgCtrl

## Slide 51
Sender Receiver
Client Server
Mode Switch
Parameter Interface
Nv Interface
Trigger Interface
Data Exchange: A sender distributes information to one or several receivers, or one receiver gets information from several senders
RPort
PPort
Operation Exchange: The server is provider of operations, and several clients can invoke those operations
Mode Exchange: The mode manager provides modes (states) that can be used by mode users to adjust the behavior according to these modes
Constant Exchange: A parameter interface allows software components access to constant data
Non-Volatile Data Write/Read: Provide element level access (read only or read/write) to non-volatile data
The trigger interface allows software components to trigger the execution of other software components
Port Interfaces Types

## Slide 52: SWCD Example
Application Component Name
Ports
Port Interface Reference

## Slide 53: Compositions
- Composition allows encapsulation of specific functionality by grouping of software components
- Compositions reduces complexity when viewing or designing application software architecture
- At least one Composition must be created “Top Level Composition”
- Compositions can be nested
SWC
SWC
SWC
SWC
SWC
SWC
DiagComposition
OBCComposition
TopLevelComposition
ErrHndlComposition

## Slide 54: Compositions

## Slide 55
Compositions
- SWCs of the same composition are connected via Assembly Connectors
- SWCs of different compositions are connected via Delegation Connectors
SWC
SWC
SWC
SWC
SWC
SWC
DiagComposition
OBCComposition
TopLevelComposition
Asm
Asm
Asm
Delg

## Slide 56
SWC
SWC
SWC
SWC
SWC
SWC
SWC
SWC
SWC
SWC
Assembly Connector (SWCs or Compositions at the same level) - P to R
Delegation Connector (SWCs or Compositions at different level) - P to P or R to R
P
R
P
P
R
R
R
P
P
Top Level Composition

## Slide 57
Seat Control
Task 1: Application Design
Design Vehicle Application to control Driver Seat

## Slide 58: Task 1: App Design
Needed Features:
Seat Height (1)
Seat Slide (4)
Seat Inclination (5)
Auto/Manual Setting
https://www.autosar.org/fileadmin/standards/R21-11/CP/AUTOSAR_EXP_AIBodyAndComfort.pdf

## Slide 59: Task 1: Solution

## Slide 60
Questions

## Slide 61
Feedback